## Slide 1: FUEL INJECTOR DIAGNOSIS

## Slide 2: INJECTION SYSTEMS AND LAB SCOPES

## Slide 3: Two Main Systems for Injector Control
Group or Bank Injection
  Groups of injectors fire together
  Each driver fires two or more injectors
Sequential Fuel Injection
  Injectors fire one at at time
  Each injector has its own driver
Type determines diagnostic method

## Slide 4: INJECTOR ELECTRICAL CIRCUITS
Conventional (Mechanical) Current Limiting
  Two mechanical methods of limiting current
    Ballast resistors
    High resistance Injectors
  Saturated Driver Circuit
    Turns injectors on and off

## Slide 5: Conventional (Saturated) Switch Injector
Injector driver constantly applies current to the injector
Use a single on-time pulse
Measure from falling edge to rising edge

## Slide 6: INJECTOR ELECTRICAL CIRCUITS
ELECTRONIC CURRENT LIMITING
  Peak and Hold
    Computer uses a “Peak Circuit” and a “Hold Circuit”
    Computer turns on both circuits to energize injector - current flow high
    Turns off “Peak Circuit”
    “Hold Circuit” reduces current flow
    Turns off “Hold Circuit” to end on-time

## Slide 7: PEAK AND HOLD INJECTOR
Uses two circuits to energize injector
After initial current flow, one circuit releases and allows second circuit to operate with lower current.
Measure on time at falling edge and off time at second spike

## Slide 8: PNP Injector
PNP driver allows reverse polarity
Driver applies current to operate injector
Single on-time pulse

## Slide 9: Pulse Modulated Peak and Hold Injector
ELECTRONIC CURRENT LIMITING
  Pulse Modulated
    Computer turns injectors on
    Computer rapidly pulses signal to limit current flow
    Computer turns injector off

## Slide 10: BOSCH PNP PEAK AND HOLD
Same as NPN but reverse polarity
Circuit is always grounded
Computer sends pulse to energize injector
Used on European cars

## Slide 11: INJECTOR DIAGNOSIS
Must have clean vertical drop on on-time pulse
Pulse much reach within 600 milli-volts of ground
Spikes should be consistent, if not may be power feed to PCM
Waveforms abnormal - Start a waveform library

## Slide 12
LAB PRACTICAL
  Get a car and hook up a lab scope to an fuel injector.
  Draw the pattern you get and identify the type of injector circuit
  Be sure to measure the amplitude and the pulse width.