## Slide 1: FUEL INJECTION SYSTEMS

## Slide 2: Types of Fuel Injection Systems
Port fuel injection. (PFI/MPFI)
Throttle Body Fuel Injection. (TBI)
Mechanical or CIS injection system.
1958 Corvette 1st fuel injection (Manual)

## Slide 3: Electronic Injection System
Electronic Parts
Computer (PCM):
  logic device.
Sensors :
  input data to the computer.
Actuators :
  output devices the computer operates.
Mechanical Parts
Fuel tank.
Fuel pump.
Fuel filter and lines.
Injector or injectors.
Fuel rail.
Pressure regulator.

## Slide 4: Electronic Parts
Electronic Parts Computer (PCM) - logic device.
Sensors
  input data to the computer.
Actuators
  output devices the computer operates

## Slide 5: Fuel Filter and Fuel Lines
Sock on gas pump
Inline
Screen in injector

## Slide 6: Fuel Rail & Pressure Regulator
The rail - pipe that fills the injectors.
Pressure regulator controls the pressure to injectors.
Pressure adjusted for changes in intake manifold vacuum.
Some are mechanical but newer cars use an electronic system.

## Slide 7: Fuel Injectors
Injectors
  electrically operated valve.
Fuel pump
  pumps fuel to injector from fuel tank
  holds pressure against e injector’s valve.
Computer triggers valve with electrical signal called a pulse.
  (pulse width)

## Slide 8: Fuel Injector Parts
“O” Ring seals
  fuel rail
  intake manifold.
Solenoid inside,
  note electrical connection.
Pintle Needle
  at spray end
  where fuel shoots out.

## Slide 9: How the Injector Fires
The computer grounds the injector to turn it “pulse” -- “Pulse width”
Pulses timed by crankshaft sensor (CKPS). And/or camshaft sensor (CPS).
Three ways to fire the injectors:
1. Group
2. Gang injection
3. Sequential injection

## Slide 10: Sensors

## Slide 11: Electronic Sensors (Inputs)
MAP Manifold Absolute Pressure
MAF Mass Air Flow
ECT Engine Coolant Temperature
IAT Intake Air Temperature
TPS Throttle Position Sensor
VSS Vehicle Speed Sensor
O2 Exhaust Oxygen Sensor
CKP Crankshaft Position
CMP Camshaft Position
KS Knock or Detonation Sensor

## Slide 12: Manifold Absolute Pressure Sensor (MAP)
Measures difference between atmospheric pressure and intake manifold vacuum.

## Slide 13: Mass Air Flow Sensor (MAF)
Measures mass of air entering intake manifold.

## Slide 14: Throttle Position Sensor (TPS)
Measure throttle angle for PCM.
Electronically: it’s a potentiometer.
The voltage signal changes as resistance in pot. changes.

## Slide 15: Engine Coolant Temperature Sensor (ECT)
Measure engines coolant temperature.
Sensor mounted in engines water jacket.

## Slide 16: Intake Air Temperature (IAT)
Works like CTS -measures - temperature of intake air.
detect intake air temperature
achieving the precise control of the A/F ratio.

## Slide 17: Vehicle Speed Sensor (VSS)
Monitors VEHICLE SPEED
NOT ENGINE SPEED

## Slide 18: Oxygen Sensor (O2 or HO2S)
Measure the amount of oxygen in the exhaust stream.
Low voltage <.45 is a lean signal.
High voltage >.45 is a rich signal.
1996 /newer use two O2 sensors.
Some O2 sensors are heated. ( HO2S)

## Slide 19: Crankshaft Position Sensor (CKP)
Uses Notches in crankshaft

## Slide 20: Camshaft Position Sensor (CMP)

## Slide 21: Knock Sensor (KS)
Senses detonation which the engine is running.
PCM will retard spark when detonation is detected.

## Slide 22: Computer Actuators (Outputs)
Fuel Injectors
IAC Idle Air Control
Fuel Pump Relay
CANP Canister Purge
EGR Regulator
Cooling Fan Relay
Torque Converter
MIL-Malfunction Indicator Lamp