## Slide 1: Sensors used in EFI (Electronic Fuel Injection)
Dr. Shahin H. Berisha
GateWay Community College
Phoenix, Arizona, USA

## Slide 2: What is EFI?
EFI is a way of delivering fuel to the engine by electronically controlling injection directly into the intake manifold near the intake valve

## Slide 3: History of EFI
Carburetors are used to mix air and fuel,
In 1979/80 Toyota introduced EFI,
By 1991 the carburetor is eliminated,
Reasons for switch:
  Superior emissions control,
  Better fuel economy,
  Improved vehicle performance

## Slide 4: How EFI Works?
There are three sub-systems in EFI
  the fuel delivery system
  air induction system
  the electronic control system

## Slide 5: Fuel Delivery System
This system consist of the:
  fuel tank,
  fuel pump,
  fuel filter,
  fuel delivery pipe,
  fuel injector,
  fuel pressure regulator, and
  fuel return pipe.

## Slide 6: The Air Induction System
This system consist of the:
  air cleaner,
  AIR FLOW METER
  throttle valve,
  air intake chamber,
  intake manifold runner, and
  intake valve.

## Slide 7: Electronic Control System
This system consist of the:
  Various engine SENSORS,
  Electronic Control Unit (ECU),
  Fuel injector assemblies, and related wiring
  The ECU determines precisely how much fuel needs to be delivered by the injector based on the engine SENSORS output. Injector is turned On for the precise amount of time to deliver proper air/fuel ratio to the engine.

## Slide 8: Basic Operation of ECU System
Air enters the engine and then measured by the AIR FLOW METER,
As the air flows into cylinder, fuel is mixed into the air by injector,
ECU pulses the injector On and OFF. When it is ON just enough spraying of fuel occurs, to ensure ideal air /fuel ratio 14.7:1
The ECU Control delivers precise amount of fuel to the engine,
The injection quantity depend on variables such as:
  coolant temperature
  engine speed (rpm)
  throttle angle,
  exhaust oxygen content.

## Slide 9: Advantages of EFI
Uniform Air/Fuel Mixture Distribution (each cylinder has its own injector),
High accurate Air/Fuel Ratio Control (better vehicle performance, better fuel economy, and emissions control)
Super throttle response,
Improved Cold Engine Startability Operation (Starting the vehicle at lower temperatures)

## Slide 10: Sensors involved in Air Induction System
Vane Air Flow Meter - consist on the:
  spring loaded measuring plate,
  potentiometer attached to the plate,
  volume of the air determines the position of the plate,
  position of the plate determines the value of the resistance on the potentiometer,
  this resistance determines the output voltage of the sensor that goes to ECU
Karman Vortex Air Flow Meter

## Slide 11: Sensors involved in Air Induction System
Karman Vortex Air Flow Meter
  the air flow generates variable frequency digital signal,
  the frequency of the digital signal is proportional to air flow

## Slide 12: Electronic Control System
This system ahs three elements:
  Input Sensors,
  ECU (a microprocessor)
  Output

## Slide 13: Input Sensors First Design Air Flow Meter
Has seven connectors, four of which are used for air flow meter,
Air flow changes the resistance of potentiometer,
This changes the voltage drop (output voltage) across the potentiometer (Vs)
Vc is used as a reference voltage because main vehicle battery Vb may change with the load.

## Slide 14: Input Sensors Second Design Air Flow Meter
Has seven connectors, three of which are used for air flow meter,
Air flow changes the resistance of potentiometer (r1 and r2),
This changes the voltage drop (output voltage) across the potentiometer (Vs)
Vc is used as a reference and a regulated 5V is used instead of Vb

## Slide 15: Input Sensors Karman Vortex Air Flow Meter
A photocoupler and a mirror
a vortex generator
and IC
When air passes through the air flow meter, the vortex generator produces digital signal
Frequency of this signal is proportional to the velocity of air

## Slide 16: Input Sensors Manifold Absolute Pressure Sensor or vacuum sensor
This sensor measures intake air volume
Consist of a piezoelectric silicon chip and an IC
Comparing the perfect vacuum and pressure in the intake manifold, the resistance of the silicon chip changes,
Change in the resistance causes change in signal voltage at PIM (Pressure Intake Mainfold) on the circuit.

## Slide 17: Water Temperature Sensor
It monitors engine coolant temperature by a thermistor with a negative temperature coefficient,
Thermistor is part of a circuit in which a voltage drop across this thermistor is monitored by ECU
As temperature goes up voltage goes down (see figure) - negative temperature coefficient

## Slide 18: Air Temperature Sensor
Monitors the temperature of air entering intake manifold by means of thermistor
It has identical characteristics as a water temperature sensor
This sensor is needed because the pressure and the density of air changes with temperature

## Slide 19: Throttle Position Sensor On-Off Type Sensor
This is a simple switch device that either pulls a reference voltage to ground (V = 0) - PSW position on the circuit or
sends a battery voltage signal to ECU - IDL position on the circuit
this switching action causes the voltage signal to ECU to go high when the switch contact are closed.

## Slide 20: Throttle Position Sensor Linear Throttle Position Sensor
As the throttle opens, a potentiometer circuit converts the mechanical movement of the throttle valve into a variable voltage signal,
The output voltage VTA is proportional with the throttle opening angle

## Slide 21: Oxygen Sensors
Exhaust oxygen sensors are used to provide air/fuel ratio feedback information to ECU,
Based on this information the ratio/fuel is adjusted continuously - Closed Loop
This idea is used in a cruise control driving
If the loop is open no information is fed into ECU
This sensor is located near the exhaust and operates at temperatures above 750oF

## Slide 22: Zirconium Dioxide Sensor
An Electro-mechanical device that compares the oxygen content of the exhaust stream with the oxygen in an ambient air sample,
This sensor act as a battery cell with two electrodes,
Output voltage is very small,
Graph shows that if air/fuel ratio is very little below or above the proper value of 14.7:1 the voltage output jumps sharply,
This is an indicator for microcomputer to activate closed loop.

## Slide 23: Titania Oxygen Sensor
This is a variable resistor,
The value of the resistance changes as the oxygen concentration of the exhaust gas changes,
As R changes, the signal voltage at the ECU also changes,
Similar to Zirconium Sesnor, the output voltage changes rapidly if air/fuel ratio is changed.

## Slide 24: Knock Sensor
This is a piezoelectric device that produces an output voltage under the vibration,
The amplitude and the frequency of vibration varies with the intensity of knock,
In one type of sensor the highest voltage output occurs around vibration with a frequency of 7 kHz
This variable frequency sensor is fed into ECU

## Slide 25: Altitude Sensor
Altitude is measured based on the oxygen density
Density of oxygen in the atmosphere is lower at high altitudes
Sensor measures the atmospheric pressure which is a function of density
In higher altitudes the injection duration is shorten